## Slide 1: MyGIS.apk
By
Thabo Maqelepo
Boocha34

## Slide 2: MyGIS Vx.x
What is it?
What Does it Do…
Application Layout
How does it do it…
What Can You Do With It…
Advantages…
Limitations…
POSSIBILITIES.

## Slide 3: What is it
MyGIS is an Android application that can be used for a multitude of Geo-related activities and applications, and some of these may include but not limited to:
Creating, viewing and editing Geospatial data
Simplified Navigation (Moving Map)
Tracking of Geo located Objects
Sharing of Geospatial data between different devices and platforms

## Slide 4: What Does it Do
MyGIS allows the user to view geo referenced maps which can be slaved to the device GPS, the maps are in plain PNG format that can either coupled with a “.pgw”projection file or a simple notepad defining the bounadry coordinates
Vector data can be displayed as a map overlay or viewed independently, using the native database format called EYEnid
MyGIS also supports Notepad and Spreadsheet CSV, DXF, KML(uncompressed) and JAVA Open Street Map (JOSM) data.
MyGIS also support XYZgrid data formats for basic 3D terrain modeling and relief analysis.

## Slide 5: What Does it Do
Users can to create geographically accurate vector data either manually by touch or automatically by GPS.
  Data can be created as either Points, Lines or Polygons.
  Data can be created against a geo-referenced Platform (Map Overlay) or based on a Fake space.
  Data can be created “In-Pocket”.

## Slide 6: What Does it Do
MyGIS allows the user to manipulate vector data
  Object vertices can be edited
  datasets can be changed to different vector types (points-to-lines-to-polygons) and their color can be changed
  Datasets can be converted to all formats supported by the App with the exceptions of Openstreet format.
  All data within its working folders can be directly deleted form the App

## Slide 7: What Does it Do
  MyGIS allows the User to Stakeout vector objects using a dynamic compass
  MyGIS includes a measurement tool where an object’s Length, Perimeter and Area can be measured by free-hand or by snapping to the objects.
  Vector Data can be shared to another MyGIS application directly via a Geo-Encoded or Geo-Packed Sms.
  Maps and orther bulk data can be transferred via the ShareIt and Whatsap Platforms*

## Slide 8: Application Layout

## Slide 9: Application Layout

## Slide 10: Application Layout
Data Access

## Slide 11: Application Layout -Key Controls
Data Access
GPS Control
Compass Control
Zoom Control*
Map Crosshairs
Pen / Manual Draw Function
GPS / Auto Draw Function
“CLUELESS Function”

## Slide 12: Application Layout -Screenshots Samples
Agricultural land mapping
Sketching the neighborhood
Searching for Trig
Pillar 9700074 /BT74

## Slide 13: Application Layout -Screenshots Samples
“One-touch” object property view
Multiple ways of finding
Pre-stored and user created vector Objects

## Slide 14: Application Layout -Screenshots Samples

## Slide 15: Application Layout -Screenshots Samples

## Slide 16: Application Layout -Screenshots Samples

## Slide 17: How does it do it
MyGIS uses a database format called EYEnid which to all application is a mere Comma Separated Plain CSV Ascii Text file.
The key to EYEnid’s applicability to a multitude of Geo-applications is in the “columns”.
ID
Major Name
Sub Name
Alpha-Color
X (Longitude)
Y(Latitude)
ZzCG Altitude / Data
Terminator

## Slide 18: How does it do it
Vertex identifier (ID)
  This is a vertex identifier that can either be unique to a single object such as a Point or represent a set of vertices as in the case of a Line or Polygon, examples of an identifier would be [pnt1000001] [lin2000002] [pol3000003].
  the first letters of the identifier indicate whether a particular vertex is a Point(pnt) , Line(lin) or a Polygon(pol) and the following numbers are random generated.

## Slide 19: How does it do it
Major Name
  This could be a generic name of an object or a number that will be treated as a sequence, example [Tree] [10001].
Minor Name
  This could be a specific object name [Pine]
Note when drawing, MyGIS does not require
the user to give the objects a name as it
will auto generate the names.

## Slide 20: How does it do it
Alpha Color (Acol)
  The color and transparency of an object
  [ARGB] = [c255181230029c] = [c255 181 230 029c]
  Alpha = 255 :000 is tranparent 255 is opaque
  Red = 181
  Green = 230
  Blue = 029
  The letters “c” are place holders to prevent 000 000 000 000
  From being truncated to 0.

## Slide 21: How does it do it
Longitude (X) Latitude (Y)
  The Coordinates are in WGS84 projection and they can be in the form dd.ddddd, dd ° mm.mm ‘, dd ° mm ' ss.sss ".
  29° 13' 35.3984" S , 28° 04' 20.3828" E
  29° 13.58997' S , 28° 4.33971' E
  29.22649956° S , 28.07232857° E

## Slide 22: How does it do it
Special Height (ZzCG)
  This column is multifunctional, could either represent height above mean sea level, relative height to a reference point or it can be to store any extra data that a particular Application function requires.

## Slide 23: How does it do it
Object Terminator (Trm)
  This is used to indicate the end of a vertex entry, this could either represent the termination of an object [eol end of line] or it could represent the end of a vertex in a series of vertices [o zero]
  In the case of singe vertex objects such as “single entry points” they end with [eol], but for series entries they will end with [0] until the last vertex which will be capped with [eol].

## Slide 24: What can YOU do with MyGIS
EVERTHING
MyGIS is primarily a GIS app
  Can be used for Viewing, Logging and Editing Geo-Data.
  Data can be captured in a multitude of ways Touch-Tap, Centering, GPS-Spot, Library Local, Geo-Sms.

## Slide 25: What can YOU do with MyGIS
Dataformats can be interchanged to ease export to other mapping platforms.
MyGIS allows for basic data statistics calculation.
Geo data can be exchange via conventional Short Message Service (SMS)!!?
And many many more…

## Slide 26: What can YOU do with MyGIS
Dynamic and hard data backup during capturing.
Global application database searching and reviewing.
Stakeout (seek out) objects by either homing or tracking.

## Slide 27: What can YOU do with MyGIS
Extra options.
Multi precision.
Audio

## Slide 28: What can YOU do with MyGIS
EVERTHING
MyGIS is primarily a GIS app
  Can be used for Viewing, Logging and Editing Geo-Data
  Data can be captured in a multitude of ways ( Touch-Tap, Centering GPS-Spot, Library Local, Geo-Sms)
Capable of Terrestrial, Arial and Marine navigation